## Slide 1: Title – Design of IOT Architecture for Battery Charging Management Technology
School of Engineering and Sciences (SEAS) Department of Electronics and Communication Engineering SRM University, Andhra Pradesh (SRM AP)
Presentation on
Prototype – Plan of Action
Presented by Jagadeesh – Jaswanth - Uttam
under the Esteemed guidance of Dr. Sujith Kalluri Ph.D Associate Professor

## Slide 2: Outline
Problem Statement
Problem Statement and Research Gap with IOT Tech
Types of Charging Technology
Scope & Deliverables
Technical Specifications
System Design
Plan of Action (4 Milestones)
Budget Breakdown
System Design
PCC integration and Automation
Automation Energy Sensor monitoring
Integrating Energy source
Automation Energy source
Load source
Discharge unit
Bill of Material’s

## Slide 3: Problem Statement Challenges in Current EV Charging Infrastructure
Grid Instability:
  High-power EV charging causes voltage fluctuations, harmonics, and transformer overloads.
High Operational Costs:
  40% higher OPEX due to grid dependency and manual monitoring.
Renewable Integration Gaps:
  No standardized system to prioritize solar/ESS over grid power.
  Excess solar energy is wasted without storage (ESS).
Battery Management:
  Lack of real-time SOC/temperature monitoring reduces battery lifespan.
User Convenience:
  Slow charging times (4–6 hours for Level-II) and range anxiety deter EV adoption.

## Slide 4
Lack of Pollution – need More Transportation – Need coal mines – More Generation cost
Why IOT needed
Real Time Data Monitoring
Pre estimation Power Demand
To Reuse Harmonic's Imbalance
Central Monitoring System
End User Integration
EV are Rapidly Increasing in the world Automotive Market
So, There is a Demand of Charging Infra
Problem Statement and Research Gap with IOT Tech

## Slide 5: Types of Charging Technology
Vehicle-to-Grid (V2G) Technology
Fast Charging Technologies
Wireless Charging
Battery Swapping
AC Charging
DC Charging
Mobile charging

## Slide 6: Scope & Deliverables
Scope:
Develop a 5-layer IoT architecture integrating solar, ESS, and grid power at PCC.
Enable real-time monitoring (SOC, temperature, energy flow) via cloud dashboards.
Optimize battery swapping (30 units) and fast charging (4 units) with predictive analytics.
Deliverables:
Functional prototype with solar (110W), ESS (12V 15Ah), and grid integration.
Automated PCC with threshold-based energy switching (80% ESS → grid feedback).
Node-RED/AWS cloud dashboard for remote monitoring.
Technical documentation (circuit diagrams, code repository, user manual).

## Slide 7: Technical Specifications
Hardware:
Solar: 110W polycrystalline panel (23.02V).
ESS: 2x 12V 15Ah lead-acid batteries.
Microcontrollers: 8x ESP32 (WiFi/Bluetooth).
Sensors: Voltage/current (ACS712), temperature (DHT11), LDR.
Software:
Node-RED: Real-time GUI.
AWS IoT Core: Cloud data storage/analytics.
Standards:
IEEE 1547 (grid integration), IEC 62196 (EV charging).

## Slide 8: System Design
Sensor Layer: Collects data (voltage, SOC, temperature).
Microcontroller Layer: ESP32 processes data.
Communication: MQTT to AWS cloud.
Cloud Layer: Stores/predicts energy demand.
UI Layer: Node-RED dashboard for operators.
Flow: Solar → ESS → Grid → Loads (swapping + fast charging).

## Slide 9: Plan of Action (4 Milestones)
Milestone 1
Generation Side
Milestone 2
PCC Automation & Loads
Milestone 3
GUI & Cloud
Procure solar panel, charge controller, ESS.
Test PCC integration (solar → ESS → grid).
Deploy 15 battery swapping units + 4 fast chargers.
Implement threshold-based automation (80%/20% SOC)
Develop Node-RED dashboard.
Configure AWS for data logging/analytics.
Milestone 4
Documentation
Finalize circuit schematics, codebase, user manual.
Prepare project report/presentation.

## Slide 10: Budget Breakdown
Hardware (₹27K):
Solar + ESS: ₹8,464 (BOM rows 5–7).
Microcontrollers/sensors: ₹8,000 (rows 16–18, 20).
Swapping/charging units: ₹8,536 (rows 3, 8–15).
Software :
AWS IoT Core (free tier + minimal costs).
Node-RED (open-source).
Miscellaneous (₹3K): PCB, wiring, tools.

## Slide 11: System Design
Solar
Fast Charging
ESS
PCC
Converter
Central Monitoring System
Grid
Swapping Station
Charging
Monitoring
Vehicles
Divider
Converter

## Slide 12: PCC integration and Automation
Start
IF
Solar Available
Load On
Grid Off
ESS Charging > 80%
IF
Solar Not Available
Grid Off
ESS ON
Load On
Power to Grid
ESS
< 20%
Grid
Power
ON
Load On
No Load
ESS Charging
Upto Solar Available
Cycle Continuous

## Slide 13: End to End Flow
Start
ESS
Solar
Check for the power source
DC Fast Charging Station
Battery Swapping Station
PCC – Point of Common Coupling
Solar – ON  ESS Charge  Grid OFF  Load ON
Solar – ON  ESS >80%  [Grid DC- AC] OFF  Load ON
Solar – OFF  ESS ON  Grid OFF  Load ON
Solar – OFF  ESS <20%  [Grid DC- AC] ON  Load ON
Solar – OFF  ESS charge  [Grid AC- DC] ON  Load OFF
Grid

## Slide 14: Automation Energy Sensor monitoring
Solar
Grid
AC
DC
DC
AC
DC – DC
Converter
SW_1
SW_2
SW_5
SW_3
SW_4
M-1
M-2
M-3
M-4
M-5
M-5
Procurement_ Part – 2
Solar
Voltage, Current, Temp, RTC, Humidity, Light Intensity, SW – M/C_1
ESS
Voltage, Current, Temp, SW – M/C_2
Grid
AC – DC - Adopter  Voltage, Current , SW – M/C_3
DC – AC Converter
Voltage, Current(AC - Sensors) SW – M/C_4
Load
DC – DC Converter
1. Swapping - Voltage, Current, SW – M/C_4
2. Fast charge – 12 Batteries Voltage, Current, SW – M/C_5

## Slide 15: Integrating Energy source
Solar
Grid
AC
DC
DC
AC
DC – DC
Converter
Procurement_ Part – 1
Sources
Solar
Pannel – 1
Solar charger converter
2. ESS
Batteries -2
Grid
AC – DC - Adopter – XHM602
DC – AC Converter
Load
DC – DC Converter
1. Swapping - 10 Batteries
2. Fast charge – 12 Batteries

## Slide 16: Automation Energy source
Solar
Grid
AC
DC
DC
AC
DC – DC
Converter
SW_1
SW_2
SW_5
SW_3
SW_4
Conditions
Solar – ON  ESS Charge  Grid OFF  Load ON - [ON – S1,S2,S5] – [OFF – S3,S4]
Solar – ON  ESS >80%  [Grid DC- AC] ON  Load ON - [ON – S1,S2,S5,S4] – [OFF – S3]
Solar – OFF  ESS ON  Grid OFF  Load ON - [ON – S2,S3,S4,S5] – [OFF – S1]
Solar – OFF  ESS <20%  [Grid DC- AC] ON  Load ON - [ON – S3,S5] – [OFF – S1,S2,S4]

## Slide 17: Load source
Procurement_ Part – 3
Swapping
batteries - 10,
Centlot xt M60312V Digital charger controller
Voltage
Current
Temperature
DC Power
M-5
M-6

## Slide 18: Load source
Procurement_ Part – 4
Swapping
batteries - 3*4 = 12,
Centlot xt M60312V Digital charger controller
Voltage
Current
Temperature
DC Power
M-5
M-7

## Slide 19: Discharge unit
Procurement_ Part – 5
Xcluma XHM240 - 18650

## Slide 20
Solar
M/c – 1
Voltage, Current, Temp, Humidity, Light Intensity, SW – On/OFF
ESS
M/c – 2
Voltage, Current, SW – On/OFF
Grid
AC – DC - Adopter  Voltage, Current , SW – M/C_3
DC – AC Converter
Voltage, Current(AC - Sensors) SW – M/C_4
M/C – 1
M/C - 2
M/C - 3
M/C - 4

## Slide 21
Swapping station
M/c – 5
Voltage, Current SW – On/OFF
Fast Charging
M/C_6
Voltage, Current, SW – M/C_4
M/C – 1
M/C - 2

## Slide 22: Load source
Procurement_ Part – 3
Swapping
batteries - 10,
Centlot xt M60312V Digital charger controller
Voltage
Current
Temperature
DC Power
M-5
M-6

## Slide 23: Bill of Material’s
S.No | Component | Qty | Specifications | Unit Cost (₹) | Total Cost (₹)
1 | Solar Panel (110W) | 1 | 23.02V, Polycrystalline | 3465 | 3465
2 | Solar Charge Controller (30A) | 2 | PWM, 12V/24V | 499 | 998
3 | Lead-Acid Battery (12V 15Ah) | 2 | Sealed, Rechargeable | 1299 | 2598
4 | ESP32 Microcontroller | 4 | WiFi + Bluetooth | 480 | 1920
5 | DC-DC Converter (1500W) | 1 | 12-48V to 24-72V Boost | 2045 | 2045
6 | Voltage/Current Sensors | 4 | ACS712 (30A), ZMPT101B (AC) | 225 | 1200
7 | Raspberry Pi 3B+ | 1 | For Real time monitoring | 4200 | 4200
 | Total | 15 |  | 12213 | 16426

## Slide 24: Thankyou
"Engineering is the closest thing to magic that exists in the world."
– Elon Musk