## Slide 1: Title – Design of IOT Architecture for Battery Charging Management Technology
School of Engineering and Sciences (SEAS) Department of Electronics and Communication Engineering SRM University, Andhra Pradesh (SRM AP)
Presentation on
Major project
Presented by Jagadeesh_(AP2312210002)
under the Esteemed guidance of Dr. Sujith Kalluri Ph.D Associate Professor

## Slide 2: Outline
Abstract
Problem Statement and Research Gap
Types of Charging Technology
Literature survey
Proposed Methodology
Conclusion
Tools used
IOT Architecture for Battery charging management
PCC integration and Automation
Algorithms
Designed Proposed Simulation Model in MATAB Simulation
Integrated PCC –Fully Automated & Logically connected
Swapping Station and DC Fast Charging
Central Monitoring Station
Calculated Spread sheet

## Slide 3: Abstract
Problem: Rapid EV adoption faces challenges like range anxiety, inconsistent charging, and limited infrastructure.
Solution: IoT-based architecture for efficient battery charging.
Features: Real-time monitoring, predictive analytics, mobile charging units, centralized cloud platform, and user-friendly mobile app.
Benefits: Enhanced user experience, optimized energy management, improved accessibility, and promotion of EVs and sustainable energy.
Significance: Addresses critical issues in EV charging, contributes to a cleaner future, and drives technological advancement.

## Slide 4
Lack of Pollution – need More Transportation – Need coal mines – More Generation cost
Why IOT needed
Real Time Data Monitoring
Pre estimation Power Demand
To Reuse Harmonic's Imbalance
Central Monitoring System
End User Integration
EV are Rapidly Increasing in the world Automotive Market
So, There is a Demand of Charging Infra
Problem Statement and Research Gap with IOT Tech

## Slide 5: Types of Charging Technology
Vehicle-to-Grid (V2G) Technology
Fast Charging Technologies
Wireless Charging
Battery Swapping
AC Charging
DC Charging
Mobile charging

## Slide 6: Literature survey
Growth of Electric Vehicles (EVs): The literature emphasizes the increasing adoption of EVs and the urgent need for more charging stations to alleviate range anxiety, with IoT technology playing a crucial role in enhancing station development and monitoring.
Power Quality Management: Research discusses the impact of EV charging on power quality, proposing active filters to mitigate harmonic distortion and improve overall power infrastructure.
Challenges in Residential Charging: High installation costs and limited charging ports are identified as barriers to home EV adoption. IoT solutions can enhance accessibility and user experience, with a holistic approach recommended for effective residential charging infrastructure.
Battery Swapping Integration: Studies explore the integration of battery swapping stations with traditional charging stations, focusing on optimal placement and operational strategies to improve efficiency and support urban mobility initiatives.
Energy Management Technologies: Various studies highlight the significance of energy management technologies in optimizing energy efficiency within renewable sectors, focusing on factors like energy information collection, economic analysis, and operational strategies for Energy Storage System (ESS) capacity planning.
Mobile Battery Swapping Services: A novel approach to battery swapping services is presented, detailing structural architecture for efficient operations, user communication via mobile applications, and analysis of power consumption and runtime for swapping units.
IoT-Enabled Continuous Monitoring: IoT technology facilitates continuous monitoring of EV charging processes, which helps prevent battery damage during charging. This capability ensures optimal charging conditions and enhances the overall lifespan and performance of EV batteries.

## Slide 7
Central Control Monitoring
Cloud
Solar
MPPT
ESS
Bi directional converter
Grid
Swapping
Fast Charging
User Interface
Buck – Boost converter
Proposed Methodology

## Slide 8: User Interface Application Layer
Cloud Server Layer Data storage
Sensor Layer
Communication Layer IoT Gateway Layer Processing Layer
Microcontroller Layer BMS Layer Data Acquisition Layer Processing Unit Layer
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
IOT Architecture for Battery charging management

## Slide 9
Collected Data
Storage
User Interface
Central control Pannel
Flow of Project

## Slide 10
Cloud Based Data Storage
Alerts
User data Visualization

## Slide 11: End to End Flow
Start
ESS
Solar
Check for the power source
DC Fast Charging Station
Battery Swapping Station
PCC – Point of Common Coupling
Solar – ON  ESS Charge  Grid OFF  Load ON
Solar – ON  ESS >80%  [Grid DC- AC] ON  Load ON
Solar – OFF  ESS ON  Grid OFF  Load ON
Solar – OFF  ESS <20%  [Grid AC- DC] ON  Load ON
Solar – OFF  ESS charge  [Grid AC- DC] ON  Load OFF
Grid

## Slide 12: PCC integration and Automation
Start
IF
Solar Available
Load On
Grid Off
ESS Charging > 80%
IF
Solar Not Available
Grid Off
ESS ON
Load On
Power to Grid
ESS
< 20%
Grid
Power
ON
Load On
No Load
ESS Charging
Upto Solar Available
Cycle Continuous

## Slide 13: Algorithms
Solar MPPT
Initialize Variables Check if input parameters VV (voltage), II (current), and TT (time) are empty.
Set default values if any parameter is empty:V=370V=370
I=0I=0, P2=0P2=0, P1=0P1=0, dP=0dP=0, d=1d=1, dd=0dd=0, n=1n=1
Check Time ConditionIf T>n∗0.02T>n∗0.02:Increment nn by 1
Update previous power values:P1=P2P1=P2
P2=V∗IP2=V∗I (Calculate current power)
Calculate Power ChangeCalculate change in power:dP=P2−P1dP=P2−P1
Adjust Duty Cycle Based on Power ChangeIf dd==0dd==0:If dP>1dP>1:Set dd=0.01dd=0.01
Increment dd by dddd
Else if dP<−1dP<−1:Set dd=−0.01dd=−0.01
Increment dd by dddd
Else:Set dd=0dd=0
If Duty Cycle Adjustment is ActiveIf (dP<1)&&(dP>-1):Set dd=0
Increment d by dd
Else:If (dP/dd)>0:Set dd=0.01
Increment d by dd
Else:Set dd=-0.01
Increment d by dd
Calculate Duty Cycle DCalculate duty cycle:D=d/(d+1)
Limit Duty Cycle ValuesIf D<0.4:Set D=0.4
Update duty cycle:d=D/(1-D)
Else if D>0.9:Set D=0.9
Update duty cycle:d=D/(1-D)
End of Algorithm Return the final value of duty cycle D.

## Slide 14: Algorithms
Battery Swapping Station -- Charging
Initialize Persistent Variables:
  Check if LoadOnPersistent and ChargingOnPersistent are empty.
  If empty, set:
    LoadOnPersistent = 1 (Load is initially ON)
    ChargingOnPersistent = 0 (Charging is initially OFF)
Check State of Charge (SOC):
  If SOC > 80:
    Set LoadOnPersistent = 1 (Turn load ON)
    Set ChargingOnPersistent = 0 (Turn charging OFF)
  Else if SOC < 40:
    Set LoadOnPersistent = 0 (Turn load OFF)
    Set ChargingOnPersistent = 1 (Start charging)
Assign Output Values:
  Assign output values:
    LoadOn = LoadOnPersistent
    ChargingOn = ChargingOnPersistent
Return Outputs:
  Return the values of LoadOn and ChargingOn.

## Slide 15: Algorithms
Car Charging control calculation
Input Parameters:
  Receive input values:
    voltage: Voltage of the battery in volts.
    current: Current flowing into the battery in amperes.
    temperature: Temperature of the battery in degrees Celsius.
Define Constants:
  Set constants for calculations:
    nominalVoltage = 12 (Nominal voltage of the battery in volts).
    maxCurrent = 100 (Maximum current rating in amperes).
    fullChargeCapacity = 100 (Full charge capacity in Ah).
    minVoltageCutoff = 10.5 (Minimum voltage cutoff for the battery in volts).
    maxCycles = 500 (Estimated maximum cycles for the battery life).
Voltage Level Calculation:
  Assign voltageLevel = voltage.
Current Level Calculation:
  Assign currentLevel = current.
  Calculation
Output Parameters:
  Return all calculated parameters:
    voltageLevel currentLevel
    SOC SOH DOD ROH
    batteryLifeCycle insulationResistance
    residualCurrentMonitoring temperatureMonitoring
    chargingTime

## Slide 16
Solar
Fast Charging
ESS
PCC
Converter
Central Monitoring System
Grid
Swapping Station
Charging
Monitoring
Vehicles
Divider
Converter

## Slide 17
Integrated PCC – Point of common coupling – Fully Automated & Logically connected
Output of PCC
Voltage 430 V
Current 80 A
Power KW/h 75 KW
Power / Day 1800 KW
Conditions
Solar – ON  ESS Charge  Grid OFF  Load ON - [ON – S1,S2,S5] – [OFF – S3,S4]
Solar – ON  ESS >80%  [Grid DC- AC] ON  Load ON - [ON – S1,S2,S5,S4] – [OFF – S3]
Solar – OFF  ESS ON  Grid OFF  Load ON - [ON – S2,S3,S4,S5] – [OFF – S1]
Solar – OFF  ESS <20%  [Grid DC- AC] ON  Load ON - [ON – S3,S5] – [OFF – S1,S2,S4]
Solar  OFF  ESS Charge  Grid ON—Load OFF
Solar
ESS
Grid
PCC
Output
Power Management

## Slide 18
State of Charge (SoC): Available battery capacity as a percentage.
Battery Voltage: Voltage of individual battery packs.
Battery Current: Charging and discharging current measurements.
Battery Temperature: Monitors battery temperature for safety.
Swapping Time: Measures time taken for each battery swap.
Energy Usage: Measures of energy consumed during swaps.
Fault Detection: Identifies issues like short circuits.
Batteries – 30
Voltage - 12
Current - 10A
Power/ battery – 0.12kw
Cars | Voltage (V) | Power (kW) | Battery Capacity (kWh) | SOC Avaliable | Required Current | Charging Time in hr | Unit charge | Cost
1 - Tata Nexon - EV | 400 | 30.2 | 30.2 | 20 | 75.5 | 2.47 | 10 | 745.83
2- MG ZS EV | 400 | 50 | 44.5 | 30 | 125 | 1.49 | 10 | 743.75
3-Tata Trigo EV | 400 | 16.8 | 26 | 50 | 42 | 4.40 | 10 | 739.58
4- Mahindra eVerito | 400 | 70 | 60 | 10 | 175 | 1.07 | 10 | 747.92
Total Power |  | 167 |  |  | Total Time | 9 | Total Revenue | 2977
Swapping Station and DC Fast Charging

## Slide 19
Central Monitoring Station
EV Parameters calculation
EV Battery charging Parameters

## Slide 20
Power Generation |  |  |  |  |  |  | PCC - Point of common coupling |  |  |  |  | ESS - Charging | 
Power Source | Voltage [V] | Current [I] | % of Generation/day | Power [P]- KWh | Power/day |  | PCC will Logically be controlled on availability of source |  |  |  |  | No.of batteries | 40
Solar | 430 | 100 | 60 | 43 | 1032 |  | Voltage - [V] | 430 | Output Power/day in KW |  |  | Voltage | 12
ESS | 480 | 50 | 30 | 24 | 576 |  | Current - [I] | 80 |  |  |  | Amper hour - capacity | 100
Grid | 435 | 20 | 10 | 9 | 209 |  | Power - [W] - KW/h | 75 | 1800 | Gen /day |  | Power / charge - Watt / hr | 48000
Total Power Generation per day in KW/24 hr |  |  |  |  | 1817 |  | Power Avaliability | 1.17 | 1772 | use / day |  | Power / one cycle charge - KW | 48
Fast Charging Station Load |  |  |  |  |  |  |  |  |  | 
Cars | Voltage (V) | Power (kW) | Battery Capacity (kWh) | SOC Avaliable | Required Current |  | Charging Time in hr |  | Unit charge | Cost
1 - Tata Nexon - EV | 400 | 30.2 | 30.2 | 20 | 75.5 |  | 2.47 |  | 10 | 745.83
2- MG ZS EV | 400 | 50 | 44.5 | 30 | 125 |  | 1.49 |  | 10 | 743.75
3-Tata Trigo EV | 400 | 16.8 | 26 | 50 | 42 |  | 4.40 |  | 10 | 739.58
4- Mahindra eVerito | 400 | 70 | 60 | 10 | 175 |  | 1.07 |  | 10 | 747.92
Total Power |  | 167 |  |  | Total Time |  | 9 |  | Total Revenue | 2977
Total Power |  | 1670 | KW power can charge / day |  | Total Time |  | 94 | / 96 hr | Total Revenue | 26794
Battery Swapping Station |  |  |  |  |  | 
Total Batteries | 30 |  |  |  |  | 
Under maintance | 0 |  |  |  |  | 
Avaliable batteries | 30 |  |  |  |  | 
Voltage | 12 |  | Total Batteries charging / day |  |  | 90
Current | 10 |  | Cost of charge per battery |  |  | 30
Time / Battery in hr | 5 |  | Total Amout Per day |  |  | 2700
No of Cycle per day | 3 |  |  |  |  | 
Power/Battery - KW | 0.12 |  |  |  |  | 
Total Station KW | 18 |  |  |  |  | 
Total Energy Required for Full Swapping Station per Day - KW | 54 |  |  |  |  | 

## Slide 21
Total Energy calculation |  |  |  | 
Power sources | KW / day | KW / Month | KW / year | KW / 5 years
Required full Power From Grid | 1,817 | 54,504 | 663,132 | 3,315,660
Solar | 1,032 | 30,960 | 376,680 | 1,883,400
ESS | 576 | 17,280 | 210,240 | 1,051,200
Grid | 209 | 6,264 | 76,212 | 381,060
Total Power saving / Day | 1,608 | 48,240 | 586,920 | 2,934,600
Total Cost / Day 12rs / unit | 21,802 | 654,048 | 7,957,584 | 39,787,920
Total Cost Saving / Day 12rs / unit | 19,296 | 578,880 | 7,043,040 | 35,215,200
Spending Amount | 2,506 | 75,168 | 914,544 | 4,572,720
Revenue |  |  |  | 
Source | Per day | Per Month | Per Year | Per 5 Years
Fast charging | 26,794 | 803,813 | 9,779,719 | 48,898,594
Battery Swapping | 2,700 | 81,000 | 985,500 | 4,927,500
Total Revenue | 29,494 | 884,813 | 10,765,219 | 53,826,094
Spending Amount | 2,506 | 75,168 | 914,544 | 4,572,720
Total Profit | 26,988 | 809,645 | 9,850,675 | 49,253,374
Chart: 
| Required full Power From Grid | Solar | ESS | Grid | Total Power saving / Day | Total Cost / Day 12rs / unit | Total Cost Saving / Day 12rs / unit | Spending Amount
Total Energy claculation Power sources
Total Energy claculation KW / day | 1816.8 | 1032 | 576 | 208.8 | 1608 | 21801.6 | 19296 | 2505.6
Total Energy claculation KW / Month | 54504 | 30960 | 17280 | 6264 | 48240 | 654048 | 578880 | 75168
Total Energy claculation KW / year | 663132 | 376680 | 210240 | 76212 | 586920 | 7957584 | 7043040 | 914544
Total Energy claculation KW / 5 years | 3315660 | 1883400 | 1051200 | 381060 | 2934600 | 39787920 | 35215200 | 4572720
Chart: 
| Per day | Per Month | Per Year | Per 5 Years
Fast charging | 26793.75 | 803812.5 | 9779718.75 | 48898593.75
Battery Swapping | 2700 | 81000 | 985500 | 4927500
Total Revenue | 29493.75 | 884812.5 | 10765218.75 | 53826093.75
Spending Amount | 2505.6 | 75168 | 914544 | 4572720
Total Profit | 26988.15 | 809644.5 | 9850674.75 | 49253373.75

## Slide 22: Automation Energy Sensor monitoring
Solar
Grid
AC
DC
DC
AC
DC – DC
Converter
SW_1
SW_2
SW_5
SW_3
SW_4
M-1
M-2
M-3
M-4
M-5
M-5
Procurement_ Part – 2
Solar
Voltage, Current, Temp, RTC, Humidity, Light Intensity, SW – M/C_1
ESS
Voltage, Current, Temp, SW – M/C_2
Grid
AC – DC - Adopter  Voltage, Current , SW – M/C_3
DC – AC Converter
Voltage, Current(AC - Sensors) SW – M/C_4
Load
DC – DC Converter
1. Swapping - Voltage, Current, SW – M/C_4
2. Fast charge – 12 Batteries Voltage, Current, SW – M/C_5

## Slide 23: Load source
Procurement_ Part – 3
Swapping
batteries - 10,
Centlot xt M60312V Digital charger controller
Voltage
Current
Temperature
DC Power
M-5
M-6

## Slide 24: Load source
Procurement_ Part – 4
Swapping
batteries - 3*4 = 12,
Centlot xt M60312V Digital charger controller
Voltage
Current
Temperature
DC Power
M-5
M-7

## Slide 25
Conclusion
Energy Source Integration
Optimized Charging Solutions
Energy Cost Saving
Future Stability with IOT Connectivity
Tools Used
MATLAB Simulation
Spreadsheet
Node Red
AWS
Future Works
1. Hardware setup

## Slide 26: Thankyou
"Engineering is the closest thing to magic that exists in the world."
– Elon Musk

## Slide 27
Technology
Regulation
Consumer Desire
Decarbonisation
Economics
Charger Rollout
Supply Chain Issues
Vehicle Charger availability
Roaming Chargers
Grid Capacity
EV Charging Growth
Drivers
Challenges